## Slide 1: Viryl-UW Project: Plan for the collection and analysis of data
Christopher Zaworski
University of Waterloo
August 2018

## Slide 2: Table of Contents
Data from the Warmtone
Other data that will be collected
Pressing information package
  Job Names
  Folder and File Names
  What’s in the PIP?
  Data in the Warmtone CSV files
Experimental Parameters
  Extruder Parameters
  Mould Parameters
  Press Parameters
  Different Vinyl Compounds
Recording of audio files
Storage, backup and sharing of data
Analysis software
  Large scale analysis
  Single audio file

## Slide 3: Data from the Warmtone
The Warmtone reads and outputs two kinds of data into the database
  Sensor data
  Parameter data
These can be exported as CSV files
The Parameter data will then be associated with an entire run of records
Can the sensor data be associated with a specific record ?
    Yes, the plan is to develop a custom script alongside Viryl’s engineers to associate sensor readings with a specific record via syncing up measurements and pressing
    As a backup this can also be done manually via timestamps, however this is not recommended

## Slide 4: Other data that will be collected
Information about the vinyl compounds used (manufacturer, batch number, colour, condition etc)
Environmental information (relative humidity and temperature can be measured by a device in the pressing room, also outputs csv files, and cross-referenced with outside weather data)
Industrial information (chiller, boiler temperatures)
How should we measure warping of records?
  Possibly by detecting a low-frequency signal in the audio of the record
  Or by some independent method and only sample a hanful of records

## Slide 5: Job Names
The name of each job shall follow the convention:
Where X is the name of the top stamper used (A, B, C or D) and Y is the name of the bottom stamper
The 4 digits following are the total number of hits on that stamper before the start of this run
Examples:
  The first run will be titled A0000B0000, which indicates A and B are producing their first records
  D1104A0064 indicates the top stamper was D which has been hit 1104 times before the start of this job and the bottom stamper is A which has been hit 64 times
X####Y####

## Slide 6
mmddyyLL_X####Y####r###Z.wav
Date of pressing
MMDDYY_X####Y####t###/
How many total
records in press run
Job Name
Date of Recording
Location recorded:
UW – University of Waterloo
VR – Viryl
Which numbered record in the run
Folder Names:
File Names:
Which side of record by stamper ID

## Slide 7: Pressing information package
sensor_values.csv
  Contains all information read by the Warmtone sensors during the pressing
setting_values.csv
  Contains all information collected about the Warmtone’s settings during the pressing
    Time per stage
    Temperature settings
vinylparameters.csv
  Contains all information about the vinyl used during the press, must be manually recorded
    Chemical/plastic name
    Colour
    New/recycled
environment.csv
  Contains all information about the temperature, humidity, weather and boiler and steamer settings.
notes.txt
Any miscellaneous notes included by the operator, to be used sparingly.
/audiofiles/
Only included once the records have been recorded.

## Slide 8: Data in the Warmtone CSV files
Extruder
Moulds
Press
sensor_values.csv:
Settings_values.csv:
MouldSteamIn_PSI,
MouldSteamIn_F,
MouldSteamOutTop_F,
MouldSteamOutBottom_F,
ExtruderFeedthroatTemp_F,
ExtruderBarrelZone1Temp_F,
ExtruderBarrelZone2Temp_F,
ExtruderBarrelZone3Temp_F,
ExtruderDieZoneTemp_F,
ExtruderPremouldTemp_F,
ExtruderMeltTemp_F
PressPosition_Inches,
PressForce_Ton,
ExtruderFeedThroatTemp,
ExtruderZone1Temp,
ExtruderZone2Temp,
ExtruderZone3Temp,
ExtruderDieZoneTemp,
ExtruderPremouldTemp,
ExtruderMeltTemp,
ExtruderDriveOpSpeed,
ExtruderMinTime,
ExtruderMaxTime,
ExtruderNumberOfStartingPucks,
ExtruderTimeAddToStartingPucks,
ExtruderTime,
ExtruderStartDelay,
HeatCycleDelay,
HeatCycleHeatTime,
HeatCycleDwellTime,
HeatCycleCoolTime,
HeatOffsetSetPoint,
HeatWaterPurgeTimeSetPoint,
HeatSteamBuildTimeSetPoint,
HeatSteamPurgeTimeSetPoint,
HeatDualDrainTimeSetPoint,
PressForce,
PressCloseToPressureSpeed,
PressCloseToLowPositionSpeed,
PressLowPositionMaxPressure,
PressCloseLowPosition,
PressCloseMidPositionSpeed,
PressMidPositionMaxPressure,
PressCloseMidPosition,
PressCloseToHighPositionSpeed,
PressHighPositionMaxPressure,
PressCloseHighPostion,
PressOpenToLowPositionSpeed,
PressOpenLowPosition,
PressOpenToMidPositionSpeed,
PressOpenMidPosition,
PressOpenToNearBottomPositionSpeed,
PressOpenNearBottomPosition,
PressOpenToBottomPositionSpeed,
PressOpenBottomPosition,
PressOpenMaxPressure,
PressRamOffsetPosition,
PressHighHighPosition,
PressAtPressureTime

## Slide 9: A note about data from the Warmtone
Most sensor data is temperature in Farenheit
Most settings are set as a time e.g.: heat time, dwell time, cool time, etc.

## Slide 10: Extruder Parameters
Barrel zones 1, 2 & 3 temperatures
Die zone (nozzle) temperature
Melt temperature (sensor)
Premould temperature
Pucksize
Feedscrew speed (Operating speed)
Delays

## Slide 11: Press Parameters
Press force in tons
Press close to pressure speed (in %)
Press high position max pressure
Press at pressure time

## Slide 12: Mould Parameters
Steam in (PSI + oF)
Steam out top and bottom (oF)
Delay
Heat Time
Dwell Time
Cool Time
Note: the cooling cycle may impact the next heating cycle

## Slide 13: Different Vinyl Compounds
It is recommended that a specific batch of vinyl is set aside and stored at viryl. Ideally this is from a trusted manufacturer, with well-documented material properties and is easy for operators to work with. This vinyl will be used in all cases that we wish to test Warmtone parameter changes, to remove the vinyl as a variable.
In contrast, tests of vinyl compounds will use identical Warmtone settings and swapping out vinyl compounds. However as the project stands, this is considered out of scope for the masters thesis for now.

## Slide 14: Recording of audio files
The record was designed to play through uninterrupted. Two groups of 7:01 tones with ~3:00 of silence between them for a total runtime of ~19 minutes per side
This means that the majority of the analysis run on the record can be automated (scripted), using the job ID to automatically match the audio recording with the Warmtone settings for analysis
As of now, we will plan to record every record pressed by the Warmtone. Most likely this will be done at UW, as the turntable and listening room is used quite frequently by the engineers at Viryl
We will need to sort out logistics of transporting and storing the records at UW

## Slide 15: Storage, backup and sharing of data
As a Student at UW I have 5 TB of cloud storage through Microsoft’s OneDrive. More than enough to store all audio, csv and research files for the duration of the project.
This also means that sharing of data can hopefully be made very easy, at least between those of us at the University
A 19 minute WAV file is ~300 mb, with roughly 4000 recordings (2000 records, two sides per record) the total storage required for this project is ~1.2 TB. Enough to be held on a simple external hard drive with cloud backups.

## Slide 16: Analysis Software
Python code will look at the audio file and the corresponding pressing information from the CSV’s automatically (by job ID)
It will have a series of standard measurements it will perform on each audio file and record into a separate CSV file that contains only the measurement values for SNR, distortion, etc
These CSV files can be analyzed and plotted as they are in python, MATLAB or Excel. However they may also be transferred easily into a database should that need arise.
Will handle the high data-volume tasks required for the regressive study of Warmtone parameters
Focused on making new insights and measurements that can later on be applied to the large scale CSV analysis
Will utilize python to build a command line interface and simple scripts for exploring specific audio files in depth
Will also be used to test out different models of vinyl properties, measurement techniques as well as other more experimental tasks
Large scale analysis (CSV files)
Individual audio file utilities

## Slide 17: Summary
The Warmtone press outputs two CSV files, one that reports the measurements made by the sensor and one that reports the settings on the machine.
  We will work with the Viryl software to be able to associate each measurement with a specific record produced during a press run.
There are roughly 18 press parameters that will be tested broken down by component: extruder (7), press (4) and mould (7).
Additional information will also be recorded such as temperature and humidity in the pressing room, as well as readings from the boiler and chiller running the presses at Viryl
When testing Warmtone parameter changes, the same batch of vinyl will be used. Testing different vinyl compounds can be done, however it would require a slightly tweaked experimental setup.
Most recordings will take place at the University, the logistics of this will need to be figured out
Data will be kept in folders MMDDYY_X####Y####t###/, will all csv and audio files required for analysis. Approx 1.2 TB of data will be produced in this study, stored locally on an external hard drive and backed up using UWaterloo’s OneDrive services
Analysis software will be written in Python, and will output all measurements into CSV files that can then be used by other software (MATLAB, Excel, database etc.) to plot and extrapolate

## Slide 18: CHRISTOPHER ZAWORSKI CJZAWORS@UWATERLOO.CA